Note:	Exit To Dos.Pif Setup

Product:	Windows OS Hardware Platforms

Date:	12 November, 1999

# Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

## Automatically booting to an Interact application on a Windows 95/98 PC platform

- Locate the Exit To Dos.pif in the Windows directory.

- Right click on the Exit To Dos.pif Icon or highlight icon and chose File and Properties.

- Choose the Program Tab.

- Choose the Advanced… button.

- Ensure MS-DOS mode check box is checked.

- Choose the Specify a new MS-Dos configuration radio button.

- You may check the Warn before entering MS-DOS mode.  This will warn you when you are exiting to DOS.

- Insert the following lines in the CONFIG.SYS for MS-DOS mode window:

SHELL=C:\COMMAND.COM /E:1024 /P

DOS=HIGH,UMB

Device=C:\WINDOWS\Himem.Sys

STACKS=9,256

FILES=30

REM DEVICE=C:\WINDOWS\EMM386.EXE NOEMS RAM x=D000-DFFF

If you are using a 3rd party communications card, that requires a base memory address, in conjunction with Interact you will want to unREM the EMM386.exe line and place the base memory address of the card at D000.

- Insert the following lines in the AUTOEXEC.BAT for MS-DOS mode window:

ECHO OFF

PROMPT $p$g

SET TEMP=C:\DOS

PATH C:\;C:\DOS;C:\CTC;C:\NET

LH C:\CTC\BIOSTSR

C:\CTC\ISVESA

IF ERRORLEVEL 1 GOTO NOVESA

GOTO YESVESA

:NOVESA

LH C:\CTC\VESA

:YESVESA

C:\CTC\MOUSE

REM ********************************************************************

REM Initialize touchscreen drivers:

REM For loading Serial Touchscreen (CTC Powerstations Only)

REM ********************************************************************

REM LH C:\TOUCH\DOX\SC3DOX.EXE /NOBOUNDS

REM ********************************************************************

REM Initialize touchscreen drivers:

REM For loading Bus Style Touchscreen (CTC Powerstations Only)

REM ********************************************************************

REM SET TBDPATH=C:\TOUCH

REM SET TBDINT=61

REM LH C:\TOUCH\TBDRIVER /A:310 /I:15

REM LH C:\TOUCH\TBMOUSE 1

REM ********************************************************************

REM Initialize touchscreen drivers:

REM For use with Universal shell units (CTC Powerstations Only)

REM ********************************************************************

REM SET TOUCH_PATH=C:\TOUCH

REM CALL %TOUCH_PATH%\TCHINIT.BAT

REM ********************************************************************

REM Sets Interact Environment Variables.  Needed for Interact to work

REM properly.

REM ********************************************************************

SET INTERACT=C:\INTERACT

SET INTERACT_FILES=C:\INTERACT\APPFILES

SET INTERACT_STARTUP=C:\STARTUP

REM ********************************************************************

REM Initialize Ethernet Card (CTC Powerstations Only)

REM ********************************************************************

REM CD \NET

REM CALL C:\NET\NET.BAT

REM ********************************************************************

REM Starting Workstation Shell used for serial downloads and

REM containing utilities for use with Powerstations.  Only use if you

REM want the operator to type in PSU to start the shell and from the

REM shell enter the Interact Application Manager.

REM (CTC Powerstations Only)

REM ********************************************************************

REM ECHO To start the PowerStation SHELL, type "PSU".

REM ********************************************************************

REM Starts Interact Application Manager so the Interact application

REM can be started automatically.

REM ********************************************************************

CD \Interact\AM

AM

If you are using a CTC Powerstation (except P50 models) you will need to unREM the appropriate

touchscreen driver line.  In Dos or Windows explorer, go to the C:\Touch directory.  If you have the files TBMouse and TBDriver and there are no other directories then you have a Bus type touchscreen.  If you have a Dox directory under Touch and do not have the TBMouse and TBDriver files then you have a Serial type touchscreen.  If you have both and you have a Touchinit.bat under the Dox directory then  you have a Universal touchscreen setup and it will call the appropriate touchscreen driver for you hardware.

- After inputting the lines for the Autoexec.bat and Config.sys press the OK button.

- Press the OK button on the Exit To Dos.pif Properties edit dialogue.

- Choose Start, Shut Down and Reboot in Dos mode.  Your PC or Powerstation will reboot in Dos mode and should now boot directly to Interact.