Note:	ML Addressing

Product:  MachineLogic

Date:	   2/19/2001

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# Introduction

This document is intended to describe the addressing format for MachineLogic.

### Memory Areas

The following memory areas are available in MachineLogic:

| Memory Type | Symbol | Size |
| --- | --- | --- |
| Inputs | I | 1024 Bytes |
| Outputs | Q | 1024 Bytes |
| Variable | M | 16384 Bytes |
| Retentive | N/A | 2048 Bytes |

Input and output memory locations will be defined by the IO configuration of your individual nodes.  Any register can be defined as Retained, however space is limited to a total of 2048 bytes of retained data.

Data Types

The following data types can be used in MachineLogic:

| Data Type | Description | Size (bits) | Range | Default Value |
| --- | --- | --- | --- | --- |
| BOOL | Boolean | 1 | 0 to 1 | 0 |
| SINT | Short Integer | 8 | -128 to 127 | 0 |
| INT | Integer | 16 | -32768 to 32767 | 0 |
| DINT | Double Integer | 32 | -2,147,483,648 to 2,147,483,647 | 0 |
| USINT | Unsigned short Integer | 8 | 0 to 244 | 0 |
| UINT | Unsigned Integer | 16 | 0 to 65535 | 0 |
| REAL | Real Numbers | 32 | -1.18X10-38 to 3.40X1038 | 0 |
| TIME | Duration | 32 | About 24 days | T#0s |
| BYTE | Bit String of Length 8 | 8 | 00 to FF | 0 |
| WORD | Bit String of Length 16 | 16 | 0000 to FFFF | 0 |
| DWORD | Bit String of Length 32 | 32 | 00000000 to FFFFFFFF | 0 |

### Addressing Format

MachineLogic data can be accessed at the following levels:

| Data Level | Symbol | Data Length |
| --- | --- | --- |
| Bit | X | 1 bit |
| Byte | B | 1 byte, 8 bits |
| Word | W | 2 bytes, 16 bits |
| Double Word | D | 4 bytes, 32 bits |

Below are some examples of MachineLogic addressing:

VAR1		AT  %IX0.0	:  BOOL;	 (*Access the first bit of the first input byte*)

VAR2		AT  %MB2	:  BYTE;	 (*Access the 2nd byte of internal variable memory*)

VAR3		AT  %MW4	:  INT;		 (*An integer variable starting at byte 4*)

VAR4		AT  %MD20  :  TIME;	 (*A time value, must be defined as double word*)