Note:	  *.PRG DOWNLOAD

Product:  CMOT

Date:	  10/23/00

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# Downloading a *.prg File to a Compumotor 6K Controller

Introduction

This application note will provide information on how to download a *.prg file from a PowerStation to a 6K controller via the Interact CMOT driver.

Methods of Downloading

6K programs can be downloaded via the Message Entry tool, or by using the Set Button.  To configure the Message Entry tool, complete the following:

Click inside of the Terminate Entry Key field.  Hit enter on your keyboard.  This will cause the entry tool to send your command after you type in the file name and press Enter.  Next, set the Message Input to the CMOT\1_DOWNLOAD command.  Be sure that the node number matches the node that is setup in the CMOT driver configuration.  Next, create two momentary pushbuttons addressed to LINK\MSG1_SEND and LINK\MSG1 _CLEAR.  These buttons will send the file to the 6K and clear the Message Entry tool.

When using this tool, the operator will have to know the name of the file prior to downloading it.  Also the user will have to type in the complete name of the file along with the extension.

To configure the Set Button, complete the following:

Complete the configuration as shown above, but substitute your 6K program name as the Setpoint Value.

Monitoring the Download

You can monitor the download status by addressing an Indicator Tool to: CMOT\DOWNLOADING.  While a download is in progress the state of the DOWNLOADING variable will change from 0 to 1.

Storing Your 6K Program File

For your file to be downloaded to the 6K you will need to copy it to the following directory of your Flash Disk:  C:\Appfiles\<Project>, where <Project> is the name of your application.