Note:	MachShop Serial TCP/IP

Product:	Machine Shop Toolbar

Date:

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

## MachineShop Serial TCP/IP Download Configuration (Windows 95/98 PC)

This application note assumes a correct installation of the MachineShop software. In order to do a Serial download to the MachineShop Shell, you must have installed:

- Internet Explorer 5.0,

- TCP/IP

- Dial-Up Networking

- Dial-Up Adapter (Windows 95/98 only)

- MachineShop Direct Connection Modem

The MachineShop setup will determine if the required communication software is installed on your system and prompts you to install any missing components.

- Make sure that you are using a Serial Null Modem Cable with Hardware Handshaking. The pinout is shown below:

- Go to the Dial-Up Networking folder found under My Computer. If you do not have the Machine Shop Phonebook Entry you will have to reinstall it. Right-Click on the Machine Shop Phonebook Entry and select Properties.

- Check to see that the settings under the General tab match those below

- Press the Configure button for MachineShop Direct Connection.

This port refers to the COM port of the Windows PC. The Maximum speed must match the baud rate specified for the PowerStation Net 1 connection in the MachineShop Shell. Press the OK button.

- Next go to the Server Types tab and make sure those settings match the ones shown below. Select the TCP/IP Settings… button.

- Again make sure the settings match. The IP address must be on the same network as the Powerstation. This means that the first three digits of the IP address must match, while the last digit should be different. The MachineShop Shell has a default IP address of 10.0.0.2 so we Specify an IP address of the Windows PC IP address to be 10.0.0.1. Press the OK button to return to the Server Type tab, and OK again to exit the MachineShop Phonebook Entry

WARNING: If you have previously configured Windows for Ethernet point to point downloads to the MachineShop Shell using the TCP/IP Ethernet Connection, then the TCP/IP Dial-Up Adapter (Serial) Connection must be a different network than the Ethernet connection. This is accomplished by the use of the IP Address and the Subnet Mask. If you have specified an IP address of 10.0.0.X using a Subnet Mask of 255.255.255.0 for the Ethernet connection then change the IP Address of the Serial connection to 11.0.0.1 so it does not conflict. Be sure to then change the IP address of the MachineShop Shell as well to 11.0.0.2

- Once you have configured the phonebook entry, you will need to configure a serial connection in the MachineShopToolbar to download to the MachineShop Shell. Launch the Machine Shop Toolbar and open the project you wish to download. Launch the Transfer Wizard from either the Transfer menu OR the Transfer Wizard button.

- Select Download to Runtime and then hit Next

9. Define New Connection

- Name your connection and make sure the Connection type is MachineShop Net (Serial/LAN)

- Select Dial-Up Networking and make sure that the MachineShop Phonebook Entry is selected

- Switch to Direct Connection (Serial) and make sure that the MachineShop Phonebook Entry is greyed out above it. Select Define runtime system now and press Details…

- The setting of 10.0.0.2 must match the IP address specified for the PowerStation Net 1 connection in the MachineShop Shell. If you have made changes based on the WARNING on page 4 then set the IP Address to 11.0.0.2 instead. Press the OK button.

- Hit the Next> button and then hit the Finish button, leaving all the entries in the Step 2 of 2 screen at their default settings.

- You will now return to the Transfer Wizard – Step 2 of 3 with your newly created connection displayed. Hit the Next> button

- Which will take you to Step 3 of 3. Hit Finish to begin downloading to the Powerstation.