Note: MachShop Ethernet Downloads TCP/IP

Product:	Machine Shop Shell

Date:

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

## MachineShop Shell Ethernet Downloads TCP/IP Setup (Powerstation)

This application note is to be used in conjunction with the MachineShop Ethernet/LAN TCP/IP Download Configuration (Windows 95/98 PC) application note. Follow the procedures in this document to configure the Powerstation first. All text in this application note was taken from the MachineShop Shell Runtime Guide manual.

MachineShop (the Shell and Toolbar) uses the standard TCP/IP protocol to communicate over ethernet connections. The TCP/IP option from the Settings submenu allows you to configure the TCP/IP settings for the runtime system. The TCP/IP settings define the connection(s) that will be used to communicate with the development system. The settings include the:

- IP address

- IP mask

- Port address, if needed

- IRQ, if needed

These settings must be configured before you can transfer files between the runtime and development systems.

1. Select the TCP/IP button from the Settings submenu. The TCP/IP Setup screen appears.

Note: Changes made to the TCP/IP Settings are written to the TCPIP.INI file located in the NET directory. Changes do not take effect until the runtime workstation reboots. A confirmation message will display when you exit the TCP/IP Setup screen, asking if you wish to reboot the system.

2. Select the ENABLE button from the TCP/IP Setup menu. The Enable TCP/IP submenu appears. Select YES. TCP/IP must be enabled (loaded into memory) on the runtime system in order for communication to occur.

3. Select the NET SETUP option from the TCP/IP Setup menu. This option is used to define and configure the network connection. Although you are given the option to configure up to three connections, only one connection can be enabled at one time. A sample TCPIP NETWORK SETUP screen is shown below:

4. CTC Tech Support recommends first configuring NET 1 only. If either NET 2 or NET 3 is configured, disable them. Select the NET 2 or 3 button to reveal the Net submenu, and then select IFACE TYPE. Choose Disable.

You are now ready to configure your NET 1 connection for Ethernet Downloads:

5. Configuration of the TCP/IP Ethernet Connection: Interface Type

Push the NET 1 button to reveal the reveal the Net submenu.

- Select the IFACE TYPE button to reveal the Interface type submenu. Choose the Interface that corresponds to the correct Revision of your Powerstation.You can determine the revision from the last 3 digits of the serial number.

NOTE #1: You do not need to manually configure the IRQ and Port Address of the I82557 Ethernet port since it resides on the PCI bus.

NOTE #2: All NE2000 cards use an IRQ of 10 and Port Address of 280 EXCEPT for revision 100-102 P1 units. They use IRQ of 10 and Port Address of 240. Bear in mind that this is only a factory software setting, and the user may change it at any time using the ethernet configuration utility located in the NET directory.

# Configuration of IP ADDRESS and IP MASK

#### TCP/IP Direct Ethernet (Point-to-Point) Connection

Using the MachineShop Shell, TCP/IP should be configured to exist on the same network as the MachineShop Toolbar.  For example, if the IP Address of the MachineShop Toolbar is set to 11.0.0.1 and the Subnet Mask is set to 255.255.255.0; the PowerStation can be configured as follows:

### IP Address: 11.0.0.2

Subnet Mask: 255.255.255.0

#### Configuration of the TCP/IP Ethernet Connection on a Company Network using a Dedicated IP Address

Using the MachineShop Shell, TCP/IP should be configured to exist on the same network as the MachineShop Toolbar.  The IP Address must be static.  For example, if the IP Address of the MachineShop Toolbar is set to 172.25.8.201 and the Subnet Mask is set to 255.255.255.0; the PowerStation can be configured as follows:

### IP Address: 172.25.8.202

Subnet Mask: 255.255.255.0

Again, no other computer on the company network may use the IP Address configured for the PowerStation.

#### Configuration of the TCP/IP Ethernet Connection on a Company Network using DHCP

Using the MachineShop Shell, TCP/IP should be configured for DHCP.  This is accomplished by specifying an IP Address of 0.0.0.0 in the MachineShop Shell IP Address.

### IP Address: 0.0.0.0

Subnet Mask: 255.255.255.0

Download Only Option

Select the DOWNLOAD ONLY button to keep the port from initializing until the Shell is loaded. You can still upload projects from the Powerstation in DOWNLOAD ONLY mode.

6. Exit the TCP/IP Setup menu by pressing the BACK menu until the Shell prompts you to reboot the workstation. Changes do not take effect until the runtime workstation reboots.

7. You are now ready to configure your Windows PC for downloading as per the Application Note. You can only download to the MachineShop Shell when it is on the menu screen. This screen has a RUN button in the top right hand corner rather than a BACK button.