Note:	DDE Server Setup Win2000

Product:	DDE Server

Date:	1/25/2002

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# Setup of DDE Server in Windows 2000

- Right-Click on My Network Places and select Properties. Right-Click on Local Area Connection and select Properties

- Make sure you have the NWLink IPX/SPX/NetBIOS Compatible Transport Protocol and select Properties. Set the Frame type: to be Ethernet 802.3. OK the selection.

- Launch the Interact DDE Server. Count how long the Splash Screen remains on the screen before it is minimized. If it minimizes immediately then the NetBIOS Adapter Number is not correct. The DDE Splash Screen must remain for more than 3 seconds. To change the Adapter number, go to the Settings menu and select NetBIOS. Change the Adapter Number. Most Windows 2000 systems use a Network Adapter Number of 3 or 4. If the setup still does not work then return to Adapter Number 0.

- You will know that the DDE Server is communicating correctly by monitoring the NetBIOS Messages window. The message DRIVER – 06H Session Open [Remote_Node_Name] will appear.

- To read numeric data from the PowerStation in Excel use the formula: =INTERACT|VALUE!’[PowerStation_NBIOS_NodeName]\[PowerStation_Driver_And_Address]. Substitute =INTERACT|TEXT! For ASCII strings.  The Client Windows in DDE Server will then return the values from the PowerStation.